## Slide 1: History and Current Challenges in the field of Robotics
Christian Siagian
(adapted from lectures by Dr. Maja Mataric &
Dr. Gaurav Sukhatme)
Univ. Southern California, CA, USA

## Slide 2: Outline
Definition of a robot
History of robotics
Sub-field in Robotics

## Slide 3: Defining “robot”
What makes a robot
Sensors, sensor space
State, state space
Action/behavior, effectors, action space
The spectrum of control

## Slide 4: Robots Today

## Slide 5: Robots Today: Anthropomorphic

## Slide 6: Robots today: Animal-like robots

## Slide 7: Why “robot”?
The term “robot” comes from Karel Capek’s 1921 play RUR (Rossum’s Universal Robots)
“robotics” first introduced by Isaac Asimov in his science fiction writing
It is most likely a combination of “rabota” (obligatory work) and “robotnik” (serf).
The kind of robotics we will talk about will move far beyond such “obligatory work.”

## Slide 8: Alternative terms
UAV: Unmanned Aerial Vehicle
UGV: Unmanned Ground Vehicle
UUV: Unmanned Undersea (underwater) Vehicle
AUV: Autonomous Underwater Vehicle

## Slide 9: What is a Robot?
A robot is a system which exists in the physical world and autonomously senses its environment and acts in it to achieve some goals.

## Slide 10: Other Definitions
A robot is a re-programmable, multi-functional, manipulator designed to move material, parts, or specialized devices though variable programmed motions for the performance of a task (Robotics Industry Association)
Robotics is the intelligent connection of perception to action (M. Brady)
Notes: Maybe put pictures or videos

## Slide 11: What Makes a Robot?
A robot consists of:
sensors
effectors/actuators
(communication)
controller
A robot is capable of:
acting autonomously
achieving goals

## Slide 12: Sensors: what can be sensed?
Depends on the sensors on the robot
The robot exists in its sensor space: all possible values of sensory readings
Also called perceptual space
Robot sensors are very different from biological ones
A roboticist has to try to imagine the world in the robot’s sensor space

## Slide 13: State: what can be known?
A sufficient description of the system
Can be:
  Observable: robot always knows its state
  Hidden/inaccessible/unobservable: robot never knows its state
  Partially observable: the robot knows a part of its state
  Discrete (e.g., up, down, blue, red)
  Continuous (e.g., 3.765 mph)

## Slide 14: Types of State
External state: state of the world
  Sensed using the robot’s sensors
  E.g.: night, day, at-home, sleeping, sunny
Internal state: state of the robot
  Sensed using internal sensors
  Stored/remembered
  E.g.: velocity, mood
The robot’s state is a combination of its external and internal state.

## Slide 15: State and Intelligence
State space: all possible states the system can be in
A challenge: sensors do not provide state!
How intelligent a robot appears is strongly dependent on how much it can sense about its environment and about itself.

## Slide 16: Internal Models
Internal state can be used to remember information about the world (e.g., remember paths to the goal, remember maps, remember friends v. enemies, etc.)
This is called a representation or an internal model.
Representations/models have a lot to do with how complex a controller is!

## Slide 17: Action/Actuation
A robot acts through its actuators (e.g., motors), which typically drive effectors (e.g., wheels)
Robotic actuators are very different from biological ones, both are used for:
  locomotion (moving around, going places)
  manipulation (handling objects)
This divides robotics into two areas
  mobile robotics
  manipulator robotics

## Slide 18: Actuators and DOF
Mobile robots move around using wheels, tracks, or legs
Mobile robots typically move in 2D (but note that swimming and flying is 3D)
Manipulators are various robot arms
They can move from 1 to many D
Think of the dimensions as the robot’s degrees of freedom (DOF)

## Slide 19: Action vs. Behavior
Behavior is what an external observer sees a robot doing.
Robots are programmed to display desired behavior.
Behavior is a result of a sequence of robot actions.
Observing behavior may not tell us much about the internal control of a robot. Control can be a black box.
black box

## Slide 20: Autonomy
Autonomy is the ability to make one’s own decisions and act on them.
For robots, autonomy means the ability to sense and act on a given situation appropriately.
Autonomy can be:
  complete (e.g., R2D2)
  partial (e.g., tele-operated robots)

## Slide 21: Control
Robot control refers to the way in which the sensing and action of a robot are coordinated.
The many different ways in which robots can be controlled all fall along a well-defined spectrum of control.

## Slide 22: A brief history of robotics
Feedback control
Cybernetics
Artificial Intelligence (AI)
Early robotics
Robotics today
  Why is robotics hard?

## Slide 23: Feedback Control
Feedback: continuous monitoring of the sensors and reacting to their changes.
Feedback control = self-regulation
Two kinds of feedback:
  Positive
  Negative
The basis of control theory

## Slide 24: - and + Feedback
Negative feedback
  acts to regulate the state/output of the system
  e.g., if too high, turn down, if too low, turn up
  thermostats, toilets, bodies, robots...
Positive feedback
  acts to amplify the state/output of the system
  e.g., the more there is, the more is added
  lynch mobs, stock market, ant trails...

## Slide 25: Uses of Feedback
Invention of feedback as the first simple robotics (does it work with our definition)?
The first example came from ancient Greek water systems (toilets)
Forgotten and re-invented in the Renaissance for ovens/furnaces
Really made a splash in Watt's steam engine

## Slide 26: Cybernetics
Pioneered by Norbert Wiener (1940s)
  (From Greek “steersman / governor” of steam engine)
Marriage of control theory (feedback control), information science and biology
Seeks principles common to animals and machines, especially for control and communication
Coupling an organism and its environment (situatedness)

## Slide 27: W. Grey Walter’s Tortoise (1950’s)
Machina Speculatrix
1 photocell & 1 bump sensor, 1 motor
Behaviors:
  seek light
  head to weak light
  back from bright light
  turn and push
  recharge battery
Reactive control

## Slide 28: The Walter Turtle in Action

## Slide 29: Braitenberg’s Vehicles
Valentino Braitenberg (early 1980s)
Extended Walter’s model in a series of thought experiments
Also based on analog circuits
Direct connections (excitatory or inhibitory) between light sensors and motors
Complex behaviors from very simple mechanisms

## Slide 30: Braitenberg’s Vehicles
Examples of Vehicles:
V1:
V2:

## Slide 31: Braitenberg’s Vehicles
By varying the connections and their strengths, numerous behaviors result, e.g.:
  “fear/cowardice” - flees light
  “aggression” - charges into light
  “love” - following/hugging
  many others, up to memory and learning!
Reactive control
Later implemented on real robots

## Slide 32: Early Artificial Intelligence
“Born” in 1955 at Dartmouth
“Intelligent machine” would use internal models to search for solutions and then try them out (M. Minsky) => deliberative model!
Planning became the tradition
Explicit symbolic representations
Hierarchical system organization
Sequential execution

## Slide 33: Artificial Intelligence (AI)
Early AI had a strong impact on early robotics
Focused on knowledge, internal models, and reasoning/planning
Basis of deliberative control in early robots

## Slide 34: Early Robots: SHAKEY
At Stanford Research Institute (late 1960s)
Vision and contact sensors
STRIPS planner
Visual navigation in a special world
Deliberative

## Slide 35: Early Robots: HILARE
LAAS in Toulouse, France (late 1970s)
Video, ultrasound, laser range-finder
Still in use!
Multi-level spatial representations
Deliberative -> Hybrid Control

## Slide 36: Early Robots: CART/Rover
Hans Moravec
Stanford Cart (1977) followed by CMU rover (1983)
Sonar and vision
Deliberative control

## Slide 37: What’s the problem?
Robot is slow in deliberation
  Based on the sense->plan->act (SPA) model
  Inherently sequential
  Planning requires search, which is slow
  Search requires a world model
  World models become outdated
  Search and planning takes too long

## Slide 38: Reactive Systems
Collections of sense-act (stimulus-response) rules
  Inherently concurrent (parallel)
  No/minimal state
  No memory
  Very fast and reactive
  Unable to plan ahead
  Unable to learn
Sentinel papers:
  Brooks, R. A., Intelligence Without Reason
  Brooks, R.A., A robust layered control system for a mobile robot.

## Slide 39: Spectrum of Control

## Slide 40: Hybrid Systems
Combine the two extremes
  reactive system on the bottom
  deliberative system on the top
  connected by some intermediate layer
Often called 3-layer systems
Layers must operate concurrently
Different representations and time-scales between the layers
The best or worst of both worlds?

## Slide 41: Behavior-Based Systems
An alternative to hybrid systems
Have the same capabilities
  the ability to act reactively
  the ability to act deliberatively
There is no intermediate layer
A unified, consistent representation is used in the whole system=> concurrent behaviors
That resolves issues of time-scale

## Slide 42: So, are we done?
Sensors are limited and crude
Effectors are limited and crude
State (internal and external, but mostly external) is partially-observable
Environment is dynamic (changing over time)
Environment is full of potentially-useful (and useless) information

## Slide 43: Nature of Sensor Data
Odometry Data
Range Data

## Slide 44: Probabilistic Robotics
Address the fundamental problem of robotics i.e. how to combat uncertainty using the tools of probability theory
The need to model errors from sensors, actuators, and dynamic environment.

## Slide 45: Recursive Bayesian Updating
Markov assumption: zn is independent of z1,...,zn-1 if we know x.

## Slide 46: Localization

## Slide 47: Navigation Challenges
Moving from place to place
Why is navigation hard?
  Limitations and errors in sensing
  Uncertainty in localization (where am I?)
  Uncertainty in map or no map
  Uncertainty in actuation

## Slide 50: Navigation Involves
Localization
Path planning
Search / coverage
Mapping
Simultaneous Localization and Mapping (SLAM)

## Slide 51: Localization
Have a map of the world, need to figure out where you are on the map.
Can use:
  Global knowledge - GPS
  Dead-reckoning - odometry
  Landmark detection
Problems:
  Estimation process is indirect
  Measurements are noisy
  Measurements are not always available

## Slide 52: Landmark Detection
Compare view of world as perceived by sensors to stored world model - try to find a match
Examples:
  Laser scans - scan matching
  Vision - visual landmarks
Problems:
  Output from sensors needs to match the format of the world model representation. (eg difficult to use vision to match to a sonar-built map)
  Data association - may parts of the environment look the same
  Environment changes - world model becomes outdated (e.g., change in lighting -> shadows change -> vision problems)

## Slide 53: Path Planning
Finding a route from start to goal location
Need a map / world model
Need localization
World is often represented as a graph (topological map)
Use graph search techniques to find path (e.g., A*)
Problems:
  Searching is slow
  Dynamic environment -> world model outdated -> need to detect changes and re-plan new route.

## Slide 54: Planning Example - PRM
Probabilistic Roadmaps
Map Building Phase
  Randomly add nodes to Cfree
  Attempt to connect to other nodes (local planner)
Query Phase
  Connect start and goal to map
  Use A* to find path from start to goal
Local Planner

## Slide 55: PRM Result
Original path
After path smoothing

## Slide 56: 3D PRM results
No Height Constraint
4m Height Constraint

## Slide 57: 3D PRM with Re-planning
Plan initial route using D*
While flying route, detect unmodeled obstacles using stereo vision.
When obstacle detected - update world model and re-plan new route using D*

## Slide 58: Dynamic Replanning

## Slide 59: Obstacle Detection
Point could
(from range sensor) Occupancy map

## Slide 60: SLAM
SLAM: simultaneous localization and mapping
To start - no map and don’t know where you are
“Chicken and egg” problem: Need map to localize, but can’t build a map if you aren’t localized
Solution: Run mapping and localization in parallel - as map accuracy improves, localization improves, which improves the map, and so on

## Slide 61: Coverage and Exploration
Try to explore an unknown area
Try to find something in an area
With map - can plan a path that covers the area
Without map - try to move in a systematic manner
  Follow boundaries
  Spiral outward
  Random motion
  E.g. - Roomba

## Slide 62: Example Exploration Results

## Slide 63: Common Navigation Challenges
Kidnapped Robot
  Robot is localized, but is then moved (without being told)
  Now it thinks it is still somewhere else - needs to re-localize
Closing the loop
  When building a map, robot returns to the same place via another route - needs to realize this is the same place, and not a new area.

## Slide 64: Monte Carlo Localization
the probability density function is represented by samples
randomly drawn from it
it is also able to represent multi-modal distributions, and thus localize the robot globally
considerably reduces the amount of memory required and can integrate measurements at a higher rate
state is not discretized and the method is more accurate than the grid-based methods
easy to implement

## Slide 65
“Probabilistic Robotics”
Bayes’ rule
p( A | B ) =
p( B | A ) • p( A )
p( B )
Definition of marginal probability
p( A ) = p( A | B ) • p(B)
S
all B
p( A ) = p( A  B )
S
all B
Definition of conditional probability
- Sebastian Thrun

## Slide 67: Monte-Carlo localization (Thrun)

## Slide 68: Monte-Carlo Localization

## Slide 69: FASTslam (Thrun)

## Slide 70: FASTslam

## Slide 71
Setting up the problem
(following slides from Jizhong Xiao, CUNY)
The robot does (or can be modeled to) alternate between
sensing -- getting range observations o1, o2, o3, …, ot-1, ot
acting -- driving around (or ferrying?) a1, a2, a3, …, at-1

## Slide 72
Setting up the problem
We want to know rt -- the position of the robot at time t
but we’ll settle for p(rt) -- the probability distribution for rt
!
What kind of thing is p(rt) ?
The robot does (or can be modeled to) alternate between
sensing -- getting range observations o1, o2, o3, …, ot-1, ot
acting -- driving around (or ferrying?) a1, a2, a3, …, at-1

## Slide 73
Setting up the problem
The robot does (or can be modeled to) alternate between
sensing -- getting range observations o1, o2, o3, …, ot-1, ot
acting -- driving around (or ferrying?) a1, a2, a3, …, at-1
We want to know rt -- the position of the robot at time t
We do know m -- the map of the environment
but we’ll settle for p(rt) -- the probability distribution for rt
!
What kind of thing is p(rt) ?
p( o | r, m )
p( rnew | rold, a, m )
-- the sensor model
-- the accuracy of desired action a

## Slide 74
Robot modeling
p( o | r, m ) sensor model
map m and location r
p( | r, m ) = .75
p( | r, m ) = .05
potential observations o

## Slide 75
Robot modeling
p( o | r, m ) sensor model
p( rnew | rold, a, m ) action model
“probabilistic kinematics” -- encoder uncertainty
red lines indicate commanded action
the cloud indicates the likelihood of various final states
map m and location r
p( | r, m ) = .75
p( | r, m ) = .05
potential observations o

## Slide 76
Robot modeling: how-to
p( o | r, m ) sensor model
p( rnew | rold, a, m ) action model
(0) Model the physics of the sensor/actuators (with error estimates)
(1) Measure lots of sensing/action results and create a model from them
theoretical modeling
empirical modeling
take N measurements, find mean (m) and st. dev. (s) and then use a Gaussian model
or, some other easily-manipulated model...
(2) Make something up...
p( x ) =
p( x ) =
0 if |x-m| > s
1 otherwise
1- |x-m|/s otherwise
0 if |x-m| > s

## Slide 77
Monte Carlo Localization
Start by assuming p( r0 ) is the uniform distribution.
take K samples of r0 and weight each with an importance factor of 1/K

## Slide 78
Monte Carlo Localization
Start by assuming p( r0 ) is the uniform distribution.
Get the current sensor observation, o1
For each sample point r0 multiply the importance factor by p(o1 | r0, m)
take K samples of r0 and weight each with an importance factor of 1/K

## Slide 79
Monte Carlo Localization
Start by assuming p( r0 ) is the uniform distribution.
Get the current sensor observation, o1
For each sample point r0 multiply the importance factor by p(o1 | r0, m)
take K samples of r0 and weight each with an importance factor of 1/K
Normalize (make sure the importance factors add to 1)
You now have an approximation of p(r1 | o1, …, m)
and the distribution is no longer uniform

## Slide 80
Monte Carlo Localization
Start by assuming p( r0 ) is the uniform distribution.
Get the current sensor observation, o1
For each sample point r0 multiply the importance factor by p(o1 | r0, m)
take K samples of r0 and weight each with an importance factor of 1/K
Normalize (make sure the importance factors add to 1)
You now have an approximation of p(r1 | o1, …, m)
Create r1 samples by dividing up large clumps
and the distribution is no longer uniform
each point spawns new ones in proportion to its importance factor

## Slide 81
Monte Carlo Localization
Start by assuming p( r0 ) is the uniform distribution.
Get the current sensor observation, o1
For each sample point r0 multiply the importance factor by p(o1 | r0, m)
take K samples of r0 and weight each with an importance factor of 1/K
Normalize (make sure the importance factors add to 1)
You now have an approximation of p(r1 | o1, …, m)
Create r1 samples by dividing up large clumps
and the distribution is no longer uniform
The robot moves, a1
each point spawns new ones in proportion to its importance factor
For each sample r1, move it according to the model p(r2 | a1, r1, m)

## Slide 82
Monte Carlo Localization
Start by assuming p( r0 ) is the uniform distribution.
Get the current sensor observation, o1
For each sample point r0 multiply the importance factor by p(o1 | r0, m)
take K samples of r0 and weight each with an importance factor of 1/K
Normalize (make sure the importance factors add to 1)
You now have an approximation of p(r1 | o1, …, m)
Create r1 samples by dividing up large clumps
and the distribution is no longer uniform
The robot moves, a1
each point spawns new ones in proportion to its importance factor
For each sample r1, move it according to the model p(r2 | a1, r1, m)

## Slide 83
MCL in action
“Monte Carlo” Localization -- refers to the resampling of the distribution each time a new observation is integrated

## Slide 84: References
Dieter Fox, Wolfram Burgard, Frank Dellaert, Sebastian Thrun, “Monte Carlo Localization: Efficient Position Estimation for Mobile Robots”, Proc. 16th National Conference on Artificial Intelligence, AAAI’99, July 1999
Dieter Fox, Wolfram Burgard, Sebastian Thrun, “Markov Localization for Mobile Robots in Dynamic Environments”, J. of Artificial Intelligence Research 11 (1999) 391-427
Sebastian Thrun, “Probabilistic Algorithms in Robotics”, Technical Report CMU-CS-00-126, School of Computer Science, Carnegie Mellon University, Pittsburgh, USA, 2000